## Slide 1
ET AI HACKATHON · PROBLEM STATEMENT 5
AirSentinel
Predicting Delhi's air quality 24-72 hours ahead, guessing why it's bad, and
turning that into GRAP-ready action — before the air, not after it.
Live scraped, zero fabricated data
3 working modules, verified end-to-end
GRAP-native, not a replacement
Master document — project status, architecture, GRAP relevance, and integration plan
2026-07-21

## Slide 2
WHY THIS MATTERS
GRAP already exists. It's just always a step behind.
13 / 17
times Delhi invoked GRAP reactively this winter — after AQI had already crossed the threshold, not before
• GRAP (Graded Response Action Plan) tells officials WHAT to do once air is already Poor, Very Poor, Severe, or Severe+.
• It does not tell them WHEN a zone will get bad, WHICH zone first, or WHY (dust vs. traffic vs. industry) — so action starts after the damage, not before it.
• That is exactly the gap AirSentinel is built to fill: a 24-72h lead time, at zone granularity, with a guessed cause — feeding GRAP better, earlier, more targeted information.
WHAT AIRSENTINEL ADDS ON TOP OF GRAP
• Not a replacement for GRAP's action ladder — a better, earlier information feed into the ladder officials already use and trust.
Source: "Delhi brought GRAP reactively after AQI crossed limit — 13 out of 17 times this winter", theprint.in
2

## Slide 3
PROJECT STATUS
Three working modules, each independently runnable
forecasting/
LIVE
• Scrapes DPCC CAAQMS live, 13 zones, hourly
• Computes official CPCB AQI per zone/day
• 24/48/72h forecast, beats persistence baseline
• CV-tuned regularization — verified anti-overfitting
vehicle_emissions/
LIVE ON DEMO DATA
• Real VAHAN RTO -> zone mapping (documented)
• Demo: real totals + real BS6 limits, not random
• Zero fabricated numbers — always cited or labeled
• Deterministic — zero overfitting risk
shared/
LIVE
• GRAP Stage Mapper (verified current 2026 thresholds)
• Alert Generator (matches official alert template)
• Forecast-driven zone urgency ranking
• Themed dashboard — renders real data only
See PROJECT_STATUS.md for the full component-by-component gap analysis against the design plan.
3

## Slide 4
MODULE 1 — FORECASTING
Predicts AQI 24-72h ahead, per zone
• Live DPCC scraper (reverse-engineered POST contract) — hourly data, all 13 zones, no hardcoded date windows.
• Official CPCB AQI formula — piecewise sub-indices, max-of-pollutants, CPCB's >=3-pollutant rule enforced.
• Gradient-boosted trees, NOT the deck's "graph+LSTM" — a deliberate call: ~45 daily points/zone can't support an LSTM without overfitting; trees are far more sample-efficient.
• Predicts a correction to persistence (not raw AQI), shrunk by a weight chosen via cross-validation that can never be selected to lose to the baseline out-of-fold.
RESULTS VS. PERSISTENCE BASELINE
Horizon
MAE improvement
Overfit gap
24h
+4.9%
+3.3%
48h
+23.2%
+16.6%
72h
+34.6%
+14.9%
24h R2 is positive for the first time (+0.03) — beats "guess the average," not just persistence.
Delivered to the satellite/enforcement track: caaqms_readings.csv (real pollutant table, 597 zone-days) — replaces
the random placeholder labels used to prove the Prithvi fine-tuning pipeline works end-to-end.
forecasting/SESSION_SUMMARY.md §5-9 has full metrics incl. accuracy/precision/recall/F1 on CPCB category.
4

## Slide 5
MODULE 2 — TAILPIPE POLLUTION
Vehicle Emission Load Model
We calculate tailpipe pollution instead of sensing it — the same way national emission inventories are built
Vehicle count
by type & fuel, per RTO
x
Emission factor
g/km, ARAI/CPCB tables
x
Avg. distance
published transport surveys
=
Vehicle Emission
Load Index per zone
TONIGHT'S DEMO DATA — REAL-WORLD-INFORMED, NOT RANDOM
• Real Delhi-wide totals: 10,370,047 two-wheelers, 3,311,579 cars (cited, VAHAN-sourced).
• Real official BS6 regulatory limits: petrol NOx 60 mg/km, diesel NOx 80 mg/km, PM 4.5 mg/km (India's mandated standard since 2020) — not estimated.
• Real published distance study: 27-33 km/day, Indian-cities two-wheelers.
• Labeled assumptions (not cited, flagged as such): totals split EVENLY across 13 zones; cars assumed 70/30 petrol/diesel. Dashboard shows an amber "DEMO DATA" badge, never green "live".
HARDCODING AUDIT
Emission factors
Real BS6 regulatory limits tonight; full ARAI table still needed
Avg. distance
Real 2-wheeler study cited; reused for cars, flagged not distinct
Vehicle counts
Real Delhi totals; even zone-split is a labeled assumption
RTO -> zone mapping
Real RTO names + documented geo reasoning, editable
The Index formula
Pure arithmetic — zero fitted parameters, zero overfitting
Without demo data the pipeline errors out with instructions rather than fabricate — demo data is opt-in, never silent.
5

## Slide 6
MODULE 3 — FUSION LAYER + DASHBOARD
Combines every track's real output into one view
GRAP Stage Mapper
Deterministic lookup, official CAQM thresholds — verified live against caqm.nic.in, current for 2026 (Stage I 201-300 ... Stage IV 451+).
Alert Generator
Templated from real computed values only — matches the design plan's own alert format (slide 8), zero invented text.
Zone Urgency Ranking
Forecast-driven sort, vehicle-load tiebreak when available — explicitly scoped as NOT the full Enforcement Zone Ranker (that stays your teammate's track).
Cross-validation scaffold
Delhi Supersite = a DPCC station, same scraper, confirmed working — but real data too sparse for a backtest tonight. SAFAR's site is down (expired TLS cert).
Dashboard
Renders whatever is real. Anything a sibling module hasn't produced yet shows an explicit "pending" badge — never a fabricated placeholder.
Design principle across all three modules: degrade to a visible "pending" state, never fabricate.
6

## Slide 7
SYSTEM ARCHITECTURE
Four layers, top to bottom — status as of today
01
DATA
SOURCES
DPCC CAAQMS
LIVE
Station weather
(temp/RH/wind)
LIVE
Sentinel-2 / 5P
imagery
TEAMMATE
VAHAN vehicle
registrations
DEMO DATA
Delhi Supersite
(= DPCC station)
SPARSE DATA
SAFAR forecasts
SITE DOWN
02
MODEL
LAYER
Forecasting Engine
24-72h/zone
LIVE
Satellite Attribution
(Prithvi)
TEAMMATE
Vehicle Emission
Load Model
DEMO DATA
Enforcement Zone
Ranker
TEAMMATE
03
FUSION
LAYER
GRAP Stage Mapper
LIVE
Cross-check vs.
Supersite & SAFAR
SCAFFOLDED
04
OUTPUT
LAYER
Official Dashboard
LIVE
Alert Generator
LIVE
API / export
NOT BUILT
Live, real data
Live/accessible, demo or sparse data
Teammate's track / not built / site down
Module folders: forecasting/ · vehicle_emissions/ · shared/ — full detail in PROJECT_STATUS.md
7

## Slide 8
OUTPUT LAYER — LIVE RIGHT NOW
AirSentinel — Delhi Operations
The ACTUAL dashboard.html output, this session's real run — vehicle load flagged honestly as demo, not green.
Delhi (active)
+ Add city (planned)
forecasting: live
caaqms current: live
vehicle emissions: live (DEMO DATA)
satellite attribution: pending
138
CITY-WIDE AVG
AQI (forecast)
1
STAGE I
0
STAGE II
0
STAGE III
0
STAGE IV
TOP ZONES NEEDING ATTENTION (24h forecast)
RANK
ZONE
FORECAST AQI
GRAP STAGE
VEHICLE LOAD
SATELLITE
#1
Wazirpur
215
Stage I — Poor
1.00 (demo)
pending
#2
Anand Vihar
193
Below GRAP
1.00 (demo)
pending
#3
Vivek Vihar
157
Below GRAP
1.00 (demo)
pending
#4
Mundka
144
Below GRAP
1.00 (demo)
pending
#5
Jahangirpuri
134
Below GRAP
1.00 (demo)
pending
Generated by shared/dashboard.py from real outputs — open shared/outputs/dashboard.html to see it live.
8

## Slide 9
WHY THIS MATTERS FOR POLICY
A concrete tool for GRAP action-plan formulation
1
Reactive -> Proactive
24-72h lead time means Stage invocation can happen BEFORE the threshold is crossed, not 13/17 times after it — directly closing the gap from slide 2.
2
City-wide -> Zone-level
GRAP restrictions today are largely city-wide/blanket. Per-zone forecasts + urgency ranking let officials target the worst zones first, instead of restricting all of Delhi for one bad pocket.
3
Guessed cause -> Targeted response
Vehicle Emission Load Index flags where tailpipe load is highest; the (planned) satellite attribution flags dust/industrial/crop-burning zones — so the RIGHT restriction (traffic vs. construction vs. burning) gets applied, not a generic one.
4
Manual drafting -> Auto-drafted alerts
The Alert Generator turns a forecast + GRAP stage into resident-ready, official-ready text in the same format CAQM already uses — cutting response lag on the communication side.
Not a GRAP replacement — a better, earlier information feed into the action framework officials already follow.
9

## Slide 10
HACKATHON EVALUATION
How AirSentinel scores against the rubric
Innovation
25%
• Shrinkage-anchored model can't lose to the baseline out-of-fold
• "Never fabricate" is architecture, not a slogan
• Real, documented RTO->zone spatial mapping
Business Impact
25%
• Targets a cited failure: 13/17 reactive GRAP calls
• Zone-level targeting vs. blanket restrictions
• Auto-drafted alerts cut official response lag
Technical Feasibility
20%
• 3 independently-runnable modules, real live data
• Scraper contract reverse-engineered, not assumed
• Beats a real baseline at all 3 horizons, just now
Scalability
15%
• Zero hardcoded absolute paths, anywhere
• National CPCB aggregator found — 300+ cities, 1 portal
• Editable-install keeps modules in sync, zero duplication
User Experience
15%
• GRAP-color dashboard, real data only, visible "pending"
• Alert text matches the format officials already use
• Planned: LLM + multi-language advisory layer
Weights per hackathon rubric: Innovation 25% · Business Impact 25% · Technical Feasibility 20% · Scalability 15% · UX 15%
10

## Slide 11
HANDOFF
What's left for your teammate, and how to plug it in
STILL TO BUILD (satellite/enforcement track)
• Finish fine-tuning Prithvi on REAL labels — caaqms_readings.csv (597 rows) was delivered to replace the random placeholder labels used to test the pipeline end-to-end.
• Output a real per-zone source_guess with a confidence score.
• Enforcement Zone Ranker: hotspot + emission (our Vehicle Load Index is ready to consume) + land-use/industry cross-check.
INTEGRATION CONTRACT
File: satellite_attribution/outputs/attribution.csv
Columns: zone, source_guess, confidence
• zone must match the 13 canonical names exactly (import from airsentinel.stations.ZONES — don't retype)
• source_guess vocabulary should match: dust, crop_burning_smoke, industrial_haze, traffic_heavy, clear
• Drop the file in place — shared/fuse.py picks it up automatically, no code change needed on our side
STEP-BY-STEP TO GO FROM "PENDING" TO "LIVE" ON THE DASHBOARD
1
Fine-tune Prithvi on real labels
2
Run inference, produce per-zone source_guess + confidence
3
Write attribution.csv in the contract schema above
4
Re-run shared.pipeline — dashboard flips to live automatically
See forecasting/data/teammate_delivery/DATA_HANDOFF.md and shared/README.md "Satellite attribution contract".
11

## Slide 12
SCALING BEYOND DELHI
Delhi first, but built to extend
REAL FINDING THIS SESSION
CPCB runs a national real-time aggregator (airquality.cpcb.gov.in/ccr) covering 300+ cities/towns in ONE
portal — not 27+ separate state scrapers. That is the recommended next integration target, not replicating
the DPCC-style reverse-engineering effort city-by-city.
CITIES WITH COMPARABLE MONITORING DENSITY TO DELHI
Delhi
~30-40 CAAQMS stations (DPCC)
Mumbai
28 CAAQMS (MPCB 14 + IITM 9 + BMC 5)
National network
423+ stations across 209+ cities, 27 states (2023, growing)
Honest caveat: only DPCC's contract was actually reverse-engineered and verified this session. Mumbai/others are cited as promising by station count, not yet verified scrapable.
HOW TO ADD A NEW CITY
• New stations.py-equivalent: zone list + station registry for that city
• Verify that city's scraping contract (or the CPCB national portal, if it proves scrapable) the same way DPCC's was reverse-engineered — same process, documented in scraper.py
• aqi.py, forecast.py, config.py need ZERO changes — already parameterized by zone/date, not Delhi-specific
• vehicle_emissions needs a new RTO-to-zone mapping for that city's transport authority, same documented-approximation method as rto_mapping.py
• shared/config.py: add the new city's forecast path — dashboard already renders per-zone, just needs a city selector added
The dashboard's "+ Add city" chip (previous slide) reflects this — a real extension point, not built yet.
12

## Slide 13
PROPOSED NEXT LAYER (NOT BUILT)
An LLM that explains, never invents
Design constraint, non-negotiable: the LLM only explains/translates numbers already computed by the real
pipeline (forecast AQI, GRAP stage, dominant source) — it never generates or guesses a pollution number itself.
CITIZEN VIEW
• "Should I go outside today / tomorrow?" — plain-language answer per zone, in Hindi, English, and extensible to other regional languages
• Red-zone highlighting on the map — worst zones visually obvious at a glance
• Personalised advisory flags (asthma, elderly, children) layered on the same real GRAP-stage advisory text already built
OFFICIAL / LAWMAKER VIEW
• Same red zones + the forecast-urgency ranking already built, prioritised for enforcement attention
• Auto-drafted official alert text (already built, slide 6) — LLM adds a plain-language "why" summary alongside it
• Recommended GRAP stage to invoke, with the reasoning (which zones, which forecast, which source) shown, not hidden
Architecture: a thin new layer reading shared/outputs/fused_zone_state.csv — doesn't touch any existing
pipeline, so it's purely additive. Explicitly future work, flagged here rather than presented as built.
Consistent with the project's core principle throughout: real numbers only, everything else is presentation.
13

## Slide 14
STATUS RECAP
Where AirSentinel stands today
DONE
• Live forecasting engine, beats baseline at all 3 horizons
• Vehicle emissions running end-to-end tonight (demo data)
• Fusion layer, GRAP mapper, alerts, dashboard — all live
• Real data delivered to satellite/enforcement track
DEMO -> REAL, NEXT
• Real VAHAN registration export (RTO-level)
• Full ARAI/CPCB emission factor table, cited
• Real per-vehicle-category distance citations
TEAMMATE'S TRACK
• Prithvi fine-tuning on real delivered labels
• Enforcement Zone Ranker (land-use/industry)
• Drop attribution.csv into the documented contract
github.com/bhavikas-loca1/airsentinel
Full detail: PROJECT_STATUS.md · forecasting/SESSION_SUMMARY.md · vehicle_emissions/README.md · shared/README.md